ZK ECU

communication protocol

V1.2

一、	ECU Interface	2

1.	TLL、RS232 or RS422	2

二、	ECU data format：	2

1.	Serial port data format：	2

2.	Use Rules	2

3.	Control Command Packet Format	2

4.	Meaning of control command data package	3

5.	ECU Status Packet Format	6

6.	ECU Meaning of status data package：	6

三、	Control mode:	9

1.	Throttle control mode - Throttle and engine status are in the same control command	9

2.	Throttle control mode –Throttle and transmitter status in different control commands	9

3.	RPM control mode	9

四、	CRC check code：	10

1.	Non lookup method	10

2.	Table lookup method	10

五、	appendix：	11

3.	Engine Status Code	11

4.	Engine fault code	12

5.	Example of control command data	12

6.	Status Data Instance	13

# ECU interface

## TLL、RS232 or RS422

# ECU data format：

## Serial port data format：

UART: 2400/4800/9600/19200/38400/57600/115200（set able）

Data length：8bit

Parity check：no

Stop bit：1/2bit（set able）

## Use Rules

- The ECU turns off the remote control signal loss detection, the protocol will automatically send the ECU status after the ECU works, and the ECU will maintain its original operating state after the control signal is lost. (This function is only supported after protocol version 5)

## Control Command Packet Format

Sending direction: flight control ->engine

The data length is 4 bytes. The data format is as follows. Command types are distinguished by IDs.

CRC check range: byte 1 to byte 2

|----------------------------------------------------------------------------------------------|

|         byte:0        |         byte:1        |      byte:2          |         byte:3        |

|----------------------------------------------------------------------------------------------|

| 7  6  5  4  3  2  1  0| 7  6  5  4  3  2  1  0| 7  6  5  4 3  2  1  0| 7  6  5  4  3  2  1  0|

|  Head (0xFF)          |Cmd ID:  0 |  reserve                          |          CRC         |

|----------------------------------------------------------------------------------------------|

|  Head (0xFF)          |Cmd ID:  1 | SW  |    Throttle                 |          CRC         |

|----------------------------------------------------------------------------------------------|

|  Head (0xFF)          |Cmd ID:  2 |  reserve  |         Param         |          CRC         |

|----------------------------------------------------------------------------------------------|

|  Head (0xFF)          |Cmd ID:  3 |  reserve                          |          CRC         |

|----------------------------------------------------------------------------------------------|

|  Head (0xFF)          |Cmd ID:  4 |  reserve  | Ignition Pump Voltage |          CRC         |

|----------------------------------------------------------------------------------------------|

|  Head (0xFF)          |Cmd ID:  5 |  reserve  | Acceleration curve    |          CRC         |

|----------------------------------------------------------------------------------------------|

|  Head (0xFF)          |Cmd ID:  6 |  reserve           |  RPM_X | SW  |          CRC         |

|----------------------------------------------------------------------------------------------|

|  Head (0xFF)          |Cmd ID:  7 |  set rpm                          |          CRC         |

|----------------------------------------------------------------------------------------------|

|  Head (0xFF)          |Cmd ID:  8 |     |        air pressure         |          CRC         |

|----------------------------------------------------------------------------------------------|

## Control Command Packet Format

Please note the supported protocol version numbers. Please check the ECU status ID6 for the current ECU protocol version number

| Command ID | Explain | Supported protocol versions |
| --- | --- | --- |
| Cmd ID: 0 | Empty loop The main engine does not control the ECU, but the ECU will return to the engine state to keep connected | 1 |
| Cmd ID: 1 | Control Engine Status (SW): 0 The serial port does not control the engine (PWM input control mode) 1 Control the engine to stop (over temperature without cooling) 2 Control the engine to enter the standby state (over temperature automatic cooling) 3 The control engine enters the running state Note: If the switch is non-zero, the servo control signal is invalid. Control engine throttle(Throttle)： Range 0~1000（means 0% ~ 100% throttle） | 1 1 1 1 1 |
| Cmd ID: 2 | Control command，parameters(Param)： Oil drain (start oil pump) Test glow plug Test main fuel valve Test gas vlave Test pump Test starter Set the status update rate 20HZ Set the status update rate 50HZ Set the status update rate 100HZ Reset fuel consumption counter Reset thrust meter 0 Pump continue on Stop pump | 1 1 1 1 1 1 1 1 1 2 2 5 5 |
| Cmd ID: 3 | Set parameter unlocking The Cmd ID 4/5 is valid only after unlocking, otherwise the ECU will not respond to the Cmd ID 4/5 | 1 |
| Cmd ID: 4 | Set Pump Voltage when Ignition Unit step 0.02V, Pump voltage=param * 0.02V Voltage range: 0.0 ~ 5.1V | 1 |
| Cmd ID: 5 | Set RPM ACC(Acceleration curve) Range：10~70 Higher value,faster acceleration,too fast of acceleration will increase risk of flame out | 1 |
| Cmd ID: 6 | Control engine state(SW): 0 invalid 1 Control the engine to stop (over temperature without cooling) 2 Control the engine to enter the standby state (over temperature automatic cooling) 3 The control engine enters the running state Note: If the SW of ID6 is non-zero (1~3), the SW in ID1 is invalid. Use this SW state to control the engine state. RPM rate（RPM_X） Range：0~6 RPM_X Engine control rpm range 0 invalid 1 0 to 40950 2 0 to 81900 3 0 to 122850 4 0 to 163800 5 0 to 204750 6 0 to 245700 Note: If RPM_ X is a non-zero, ID1 command is invalid, use SW of ID6 to control engine status, and use RPM of ID7 to control engine speed. RPM_ Refer to RPM interpretation of ID7 for the meaning of X value. | 4 4 |
| Cmd ID: 7 | Control engine RPM（RPM） Range：0~4095 Engine RPM = RPM * 10 * RPM_X Note: Select the appropriate RPM according to the maximum engine speed_ X。 When RPM_ When X is 0, the RPM of ID7 is invalid. | 4 |
| Cmd ID: 7 | Set ambient atmospheric static pressure（air pressure） Range：0~1024 Unit:hPa |  |

## 5 Status Packet Format

Sending direction: engine ->flight control

The data length is 7 bytes, and the data format is as follows

CRC check range: byte 0 to byte 5

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//|         byte:0        |   byte:1   |   byte:2   |         byte:3        |         byte:4        |         byte:5        |       byte:6          |

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//| 7  6  5  4  3  2  1  0|   7 -- 0   |   7 -- 0   | 7  6  5  4  3  2  1  0| 7  6  5  4  3  2  1  0| 7  6  5  4  3  2  1  0| 7  6  5  4  3  2  1  0|

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//|Head (0xF0) |  ID: 1   |  RPM(LSB)  |  RPM(MSB)  |ECode   | Engine State |  |SwSt |  Temp  |ECode|         Temp          |          CRC          |

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//|Head (0xF0) |  ID: 2   |  RPM(LSB)  |  RPM(MSB)  |Radio Voltage          | Power Voltage         | Pump Voltage 0~25V    |          CRC          |

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//|Head (0xF0) |  ID: 3   |  RPM(LSB)  |  RPM(MSB)  |Throttle               | Pressure (LSB)        | Pressure (MSB)        |          CRC          |

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//|Head (0xF0) |  ID: 4   |  RPM(LSB)  |  RPM(MSB)  |Current                | Thrust(MSB)        |C | Thrust(LSB)           |          CRC          |

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//|Head (0xF0) |  ID: 5   |  RPM(LSB)  |  RPM(MSB)  |Ign Pump Voltage       | Curve INC             | Curve DEC             |          CRC          |

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//|Head (0xF0) |  ID: 6   |  RPM(LSB)  |  RPM(MSB)  |Max Rpm                | Max Pump Voltage      |Protocol Version |SRate|          CRC          |

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//|Head (0xF0) |  ID: 7   |  RPM(LSB)  |  RPM(MSB)  |    Flow Rate          | FlowTotal    |FlowRate|   Flow Total          |          CRC          |

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//|Head (0xF0) |  ID: 8   |  RPM(LSB)  |  RPM(MSB)  |Idle Rpm               |    |ESR|SCL|       Startup Time (0.1s)        |          CRC          |

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

//|Head (0xF0) |  ID: 9   |  RPM(LSB)  |  RPM(MSB)  |ECU Temperature        |                  reserve                      |          CRC          |

//|-------------------------------------------------------------------------------------------------------------------------------------------------|

## 6ECU Meaning of status data package：

Please note the supported protocol version numbers. Please check the ECU status ID6 for the current ECU protocol version number

| 命令ID | 说明 | 支持的协议版本 |
| --- | --- | --- |
| Cmd ID: 1 | // - RPM: engine rpm VAL = {BYTE2[7:0],BYTE1[7:0]} * 10 Engine State: engine state VAL = {BYTE3[4:0]} ECode: error code VAL = {BYTE4[1:0],BYTE3[7:5]} Temp: Engine exhaust temp（centigrade） VAL = {BYTE4[4:2],BYTE5[7:0]} – 50 SwSt: (computer or flight controller)send to ECU of controlstate VAL = {BYTE4[6:5]} 0: engine stop 1：engine standby 2：startup/running | 1 1 1 1 1 |
| Cmd ID: 2 | RPM: RPM: engine rpm VAL = {BYTE2[7:0],BYTE1[7:0]} * 10 Radio Voltage: receiver battery voltage VAL = {BYTE3[7:0]} Unit:0.1V VAL = {BYTE3[7:0]} Unit:0.2V Power Voltage：power battery voltage VAL = {BYTE4[7:0]} Unit:0.1V VAL = {BYTE4[7:0]} Unit:0.2V Pump voltage: pump voltage real time VAL = {BYTE5[7:0]} Unit:0.1V VAL = {BYTE5[7:0]} Unit:0.2V | 1 <=3 >=4 <=3 >=4 <=3 >=4 |
| Cmd ID: 3 | RPM: RPM: engine rpm VAL = {BYTE2[7:0],BYTE1[7:0]} * 10 Throttle: throttle VAL = {BYTE3[7:0]} Unit:% Pressure: air pressure VAL = {BYTE5[7:0],BYTE4[7:0]} * 2 Unit:Pa | 1 1 1 |
| Cmd ID: 4 | RPM: RPM:engine rpm VAL = {BYTE2[7:0],BYTE1[7:0]} * 10 Current: ECU amp real time VAL = {BYTE4[ 0],BYTE3[7:0]} Unit:0.1A Thrust: engine thrust,if without sensor,output=0 VAL = {BYTR4[7:1],BYTE5[7:0]} Unit:0.1Kg | 1 1 2 |
| Cmd ID: 5 | RPM:engine rpm VAL = {BYTE2[7:0],BYTE1[7:0]} * 10 Ignition Pump Voltage: pump voltage for ignition VAL = {BYTE3[7:0]} * 2 Unit:0.01v Curve Increase: rpm acc parameter VAL = {BYTE4[7:0]} Curve Decrease：rpm dec parameter VAL = {BYTE5[7:0]} | 1 1 1 1 |
| Cmd ID: 6 | RPM:engine rpm VAL = {BYTE2[7:0],BYTE1[7:0]} * 10 Max RPM: engine max rpm VAL = {BYTE3[7:0]} * 1000 Unit:RPM Max Pump Voltage:max pump voltage VAL = {BYTE4[7:0]} Unit:0.1V VAL = {BYTE4[7:0]} Unit:0.2V Protocol Version：Protocol Version VAL = {BYTE5[7:2]} SRate: data update rate VAL = {BYTE5[1:0]} 0: 20Hz 1: 50Hz 2:100Hz | 1 1 1 <=3 >=4 1 1 |
| Cmd ID: 7 | RPM:engine rpm VAL = {BYTE2[7:0],BYTE1[7:0]} * 10 Flow Rate: fuel flow rate VAL = {BYTR4[1:0],BYTE3[7:0]} Unit:0.01L/min Flow Total:fuel consumption counter VAL = {BYTE5[7:0],BYTE4[7:2]} Unit:0.1L | 2 2 2 |
| Cmd ID: 8 | RPM:engine rpm VAL = {BYTE2[7:0],BYTE1[7:0]} * 10 Max RPM: engine idle rpm VAL = {BYTE3[7:0]} * 1000 Unit:RPM ESR: ask flight controller send air pressure data VAL = {BYTE4[5]} 0：don’t send 1：need to send SCL: rpm close loop state VAL = {BYTE4[4]} 0：rpm open loop state 1：rpm close loop stat Startup Time: engine startup time VAL = {BYTE4[3:0], BYTE5[7:0]} Unit:0.1s | 3 3 4 4 4 |
| Cmd ID: 9 | RPM:engine rpm VAL = {BYTE2[7:0],BYTE1[7:0]} * 10 ECU Temperature: ECUtemp（centigrade） VAL = {BYTE3[7:0]} - 50 reserve: reserve {BYTE4[7:0]} {BYTE5[7:0]} | 5 5 5 |

# Control mode:

## Throttle control mode- Throttle and engine status are in the same control command

Engine state：ID1 - SW

Engine throttle：ID1– Throttle

## Throttle control mode –Throttle and transmitter status in different control commands

Engine state：ID6 - SW

Engine throttle：ID1– Throttle

## RPM control mode

Engine state：ID6 - SW

Engine rpm：ID7– RPM

RPM rate：ID6 – RPM_X （RPM_X non-zero，enter rpm control mode）

Target rpm= [ID7:RPM] * [ID6:RPM_X] * 10

# CRC check code：

## Non table lookup method

t_u8 crc8(t_u8 *puchMsg,t_u8 crc_len, t_u8 seed)

{

t_u8 i,k,crc8 = seed;

for(i = 0; i<crc_len; i++)

{

k = puchMsg[i] ^ crc8;

crc8 = 0;

if (k & 0x01) crc8 ^= 0x5e;

if (k & 0x02) crc8 ^= 0xbc;

if (k & 0x04) crc8 ^= 0x61;

if (k & 0x08) crc8 ^= 0xc2;

if (k & 0x10) crc8 ^= 0x9d;

if (k & 0x20) crc8 ^= 0x23;

if (k & 0x40) crc8 ^= 0x46;

if (k & 0x80) crc8 ^= 0x8c;

}

return crc8;

}

## Table lookup method

const t_u8 crc_array[] = {

0x00, 0x5e, 0xbc, 0xe2, 0x61, 0x3f, 0xdd, 0x83,

0xc2, 0x9c, 0x7e, 0x20, 0xa3, 0xfd, 0x1f, 0x41,

0x9d, 0xc3, 0x21, 0x7f, 0xfc, 0xa2, 0x40, 0x1e,

0x5f, 0x01, 0xe3, 0xbd, 0x3e, 0x60, 0x82, 0xdc,

0x23, 0x7d, 0x9f, 0xc1, 0x42, 0x1c, 0xfe, 0xa0,

0xe1, 0xbf, 0x5d, 0x03, 0x80, 0xde, 0x3c, 0x62,

0xbe, 0xe0, 0x02, 0x5c, 0xdf, 0x81, 0x63, 0x3d,

0x7c, 0x22, 0xc0, 0x9e, 0x1d, 0x43, 0xa1, 0xff,

0x46, 0x18, 0xfa, 0xa4, 0x27, 0x79, 0x9b, 0xc5,

0x84, 0xda, 0x38, 0x66, 0xe5, 0xbb, 0x59, 0x07,

0xdb, 0x85, 0x67, 0x39, 0xba, 0xe4, 0x06, 0x58,

0x19, 0x47, 0xa5, 0xfb, 0x78, 0x26, 0xc4, 0x9a,

0x65, 0x3b, 0xd9, 0x87, 0x04, 0x5a, 0xb8, 0xe6,

0xa7, 0xf9, 0x1b, 0x45, 0xc6, 0x98, 0x7a, 0x24,

0xf8, 0xa6, 0x44, 0x1a, 0x99, 0xc7, 0x25, 0x7b,

0x3a, 0x64, 0x86, 0xd8, 0x5b, 0x05, 0xe7, 0xb9,

0x8c, 0xd2, 0x30, 0x6e, 0xed, 0xb3, 0x51, 0x0f,

0x4e, 0x10, 0xf2, 0xac, 0x2f, 0x71, 0x93, 0xcd,

0x11, 0x4f, 0xad, 0xf3, 0x70, 0x2e, 0xcc, 0x92,

0xd3, 0x8d, 0x6f, 0x31, 0xb2, 0xec, 0x0e, 0x50,

0xaf, 0xf1, 0x13, 0x4d, 0xce, 0x90, 0x72, 0x2c,

0x6d, 0x33, 0xd1, 0x8f, 0x0c, 0x52, 0xb0, 0xee,

0x32, 0x6c, 0x8e, 0xd0, 0x53, 0x0d, 0xef, 0xb1,

0xf0, 0xae, 0x4c, 0x12, 0x91, 0xcf, 0x2d, 0x73,

0xca, 0x94, 0x76, 0x28, 0xab, 0xf5, 0x17, 0x49,

0x08, 0x56, 0xb4, 0xea, 0x69, 0x37, 0xd5, 0x8b,

0x57, 0x09, 0xeb, 0xb5, 0x36, 0x68, 0x8a, 0xd4,

0x95, 0xcb, 0x29, 0x77, 0xf4, 0xaa, 0x48, 0x16,

0xe9, 0xb7, 0x55, 0x0b, 0x88, 0xd6, 0x34, 0x6a,

0x2b, 0x75, 0x97, 0xc9, 0x4a, 0x14, 0xf6, 0xa8,

0x74, 0x2a, 0xc8, 0x96, 0x15, 0x4b, 0xa9, 0xf7,

0xb6, 0xe8, 0x0a, 0x54, 0xd7, 0x89, 0x6b, 0x35,

} ;

t_u8 crc8(t_u8 *puchMsg,t_u8 crc_len, t_u8 seed)

{

t_u8 i,crc8 = seed;

for(i = 0 ; i<crc_len; i++)

{

crc8 = crc_array[crc8^puchMsg[i]];

}

return crc8;

}

# appendix：

## engine error code

| ID | State |
| --- | --- |
| 0 | Stop/ No automatic cooling |
| 1 | Stop/ automatic cooling |
| 2 | Ignition（must throttle to min） |
| 3 | Iginition |
| 4 | Preheat |
| 5 | Ramp up |
| 6 | Running（learning mode,need throttle to max） |
| 7 | Running（Learning mode,need throttle to min） |
| 8 | Running（Learning idle） |
| 9 | Running（throttle to min） |
| 10 | Running（warring,pump to max limit） |
| 11 | Running |
| 12 | Cooling |
| 13 | Re-startup |
| 14 | Test glow plug |
| 15 | Test fuel valve |
| 16 | Test gas valve |
| 17 | Test pump |
| 18 | Test starter |
| 19 | Clear air from Fuel line system |

## Engine error code

| ID | Error message |
| --- | --- |
| 0 | No error |
| 1 | Time out |
| 2 | Low battery |
| 3 | glow plug bad |
| 4 | Pump anomaly |
| 5 | Starter failure |
| 6 | RPM low |
| 7 | RPM instability |
| 8 | High temp |
| 9 | Low temp |
| 10 | Temp sensor fail |
| 11 | Gas valve bad |
| 12 | Fuel valve bad |
| 13 | Lost signal |
| 14 | Starter temp high |
| 15 | Pump temp high |
| 16 | Clutch failure |
| 17 | Current overload |
| 18 | Engine off line |

## Example of control command data

EX1：0xFF 0x14 0x64 0xD3

Cmd ID:  1

SW:       1

Throttle: 100

EX2：0xFF 0x1D 0xF40x70

Cmd ID:   1

SW:       3

Throttle: 500

## ECU Status Data Instance

ex1：0xF1 0x00 0x000x000x000x4C 0xA0

ID:   1

RPM:  0                engine rpm

Engine State: 0       engine state(stop)

ECode: 0               error code

Temp: 26℃ engine exhaust temp（centigrade）

SwSt: 0                flight controller send control state to ECU(stop)

ex2：0xF6 0x00 0x00 0xA0 0x00 0x10 0xAB

ID:   6

RPM:  0                engine rpm

Max RPM: 160000 engine max rpm

Max Pump Voltage: 0.0V  Max Pump Voltage

Protocol Version: 4 Protocol Version

SRate: 20Hz data update rate